## Slide 1: Non-Exponential T2* Decay in White Matter
P. van Gelderen1, J. A. de Zwart1, J. Lee1,3, P. Sati1, D. S. Reich1, and J. H. Duyn1.
1 Advanced MRI section, LFMI, NINDS, National Institutes of Health, Bethesda, MD, United States
2 Translational Neuroradiology Unit, Neuroimmunology Branch,
NINDS, National Institutes of Health, Bethesda, MD, United States
3 Department of Radiology, University of Pennsylvania, PA, United States
I have no conflict to report regarding this presentation.

## Slide 2: Introduction
Measuring myelin content in the brain is important for many neurological diseases, most notably Multiple Sclerosis
Magnetization transfer {1} can be used as a measure for large molecules, e.g. proteins and fatty acids as found in myelin
T1 and T2 contrast have been proposed {2,3} as measure of a myelin water fractio and thus as a more specific measure of myelin volume and condition
The water between myelin layers is thought to have a faster relaxation and may be detectable as a separate component in the decay
1) Wolff, Balaban. MRM 10:135. 2) Deoni et.al. MRM 60:1372. 3) MacKay et.al. MRM 31:673.

## Slide 3: Introduction II: T2*
T2* measurements have been proposed at 3T {4} for the detection of myelin water
Potential advantages: simple multi gradient echo acquisition, high SNR
Higher field strength should increase SNR and potentially the separation of components, as the field inhomogeneity induced part of T2* (sometime labeled T2’) results in a faster with higher field strength
4) Hwang D, Kim DH, Du YP. Neuroimage 52:198.

## Slide 4: Goal
Explore the potential of myelin water detection using the T2* decay at 7T
Method:
Analyze multi gradient echo signal decay at 7T in human brain for the presence of a short (fast decaying) component that can be separated from the main component in the T2* decay

## Slide 5: Methods
Equipment: GE 3T and 7T with Nova Medical 32 channel receive array
Subjects: 7T: 3 female, 4 male, ages 33-54, average age 41, one scanned twice 3T: 1 female, 3 male, ages 24-45, average 36 years, 3 out of 4 participated in 7T study as well
Sequence: monopolar multi gradient echo, 256x96 resolution, 240x180mm2 FOV, 30° flip angle, TR 70ms, 1 axial slice, 50 averages, 18 echoes, TE from 2.7ms to 45ms (2.35ms spacing)

## Slide 6: Results I
Example of T2* decay, showing every other echo, TE (in ms) is indicated in the images.

## Slide 7: Results II
Residue after mono-exponential fit, scaled to +/- 6% of baseline. Note the changes in contrast, especially in the first echo when compared to later echoes.

## Slide 8: Results III
Left: signal decay in the (splenium of the) corpus callosum, with mono-exponential fit (excluding the first two echoes).
Right: the relative difference between the data and the mono-exponential fit in the splenium of the corpus callosum (black), posterior white matter (blue) and posterior internal capsule (green), showing the deviation at both short and long TE and illustrating the orientation effect (the corpus callosum is perpendicular to the field, the internal capsule parallel, the posterior white matter is mixed).

## Slide 9: Results IV
Comparison of the residue after mono-exponential fitting of the decay for 7T and 3T for a corpus callosum ROI. The short component in the 3T data appears slower than the 7T version and of somewhat reduced amplitude. Both effects are likely a consequence of the field dependence of the T2* decay. The decay rate of the short component scales with field strength. The decay rate of main component (which dominates the signal and fitting) is limited by the (field independent) T2 decay, which means the separation between the short and main T2* is smaller at 3T. The smaller separation may have reduced the amplitude of the short component apparent in the residue.

## Slide 10: Results V
Fitting results for a three component model {5}, for the average signal in the splenium of the corpus callosum. Left is the data and the fitted curve, right the residue. Although the fit is close, there is clearly a significant deviation from the model. The error bars indicate the standard error over the 8 studies.
5) Lancaster JL, Andrews T, Hardies LJ, Dodd S, Fox PT. J MRI 17:1.

## Slide 11: Results VI
Fitting results for a new three component model for the same data (corpus callosum). The new model fits the decay curve more accurately as is apparent from the smaller (and noisier) residue. This model includes offset frequencies for the two smaller components (1 and 3). The main component (2) does not have phase or frequency, as we use the magnitude of the data.

## Slide 12: Results VII
The average and SD (over subjects) of the multi compartment model parameters for two field strength (3 components for 7T, two for 3T) fitted to the averaged signal decays in the splenium of the corpus callosum.

## Slide 13: Discussion I
The T2* decay does show a deviation from mono-exponential decay in white matter
At higher field strength the short component decays faster and has a better separation from the main signal
The short component amplitude appears heterogeneous within the white matter, and is likely dependent on the orientation of the fiber bundles with respect to the main magnetic field
A multi-component model, which includes a frequency offset for the smaller components, describes the data better than the previous models without a frequency offset

## Slide 14: Discussion II
The observed third (long T2*) component may be due to CSF or other ‘free’ water, or alternatively could stem from non-exponential decay due to macroscopic susceptibility effects, which could induce a sinc-type decay resulting in a deviation from exponential shape for the later TEs.
Difference with an earlier report {4}, which shows a stronger and more homogeneous effect for the short component in the T2* decay, may be due to the applied processing in that report (anisotropic diffusion filtering on the data before fitting and voxel by voxel fitting of a three component model).
For more details and discussion, see {6}.
4) Hwang D, Kim DH, Du YP. Neuroimage 52:198. 6) P van Gelderen et.al., MRM 2011, in press.

## Slide 15: Conclusion
Higher field T2* decay can be used to detect a short component likely related to myelin water
The observed contrast is heterogeneous and likely orientation dependent, which has to be taken into account when estimating relative myelin content in different brain areas